## Slide 1
The EIC Detector R&D Program
Status, Impact, and Needs
Thomas Ullrich, BNL/Yale
EIC User Meeting Trieste
July 20, 2017
See also plenary talks by: Maxim Titov (MPGDs), Tom Hemmick (TPC), Paolo Cameron (MAPS) and Parallel 1 on Friday.

## Slide 2: EIC Detector R&D Efforts
Generic EIC Detector R&D Program (covered here)
Other substantial efforts with impact on EIC
  Laboratory Directed Research & Development Programs (LDRDs) at National Labs in the US (BNL, JLAB, ANL, …)
  CERN supported detector R&D program with partial match with EIC needs (e.g. RD51 Micro-Pattern Gas Detectors Technologies) → Maxim’s talk
  LHC Experiments R&D for phase-I upgrades, especially ALICE (TPC, ITS, SAMPA, …) and LHCb (RICH, trigger less DAQ, electronics, …). Now in production, R&D finished.
  R&D at Belle-II and Panda (crystals, DIRC, …)
  ILC related R&D (TPC, …)
    Rate and precision requirements compatible
    Less emphasis on forward/backward instrumentation
Notes: DIRC = Detection of Internally Reflected Cherenkov light

## Slide 3: Generic Detector R&D for an EIC
In January 2011 BNL, in association with JLab and the DOE Office of NP, announced a generic detector R&D program to address the scientific requirements for measurements at a future EIC
Goals of Effort
Enable successful design and timely implementation of an EIC experimental program
  Quantify the key physics measurements that drive instrumentation requirements
  Develop instrumentation solutions that meet realistic cost expectations
Stimulate the formation of user collaborations to design and build experiments
Program coordinator 2011-2014: Tom Ludlam
          2014-present: TU

## Slide 4: Generic Detector R&D for an EIC
Current: Marcel Demarteau** (ANL), Carl Haber (LBNL), Peter Krizan (Ljubljana),
Ian Shipsey (Oxford), Rick Van Berg (UPenn), Jerry Va’vra (SLAC), Glenn Young (JLab)
Retired:
Robert Klanner (Hamburg),
Howard Wieman (LBL)
* During 2011-2014 new proposals were also accepted in the Winter meeting
**Chair
  Funded by DOE through RHIC operations funds: ~$1M/year
  Program explicitly open to international participation
  Key to success: Standing EIC Detector Advisory Committee consisting of internationally recognized experts in detector technology and collider physics
    Meets twice a year, funding limited to one year (FY)
      ~January: Review of ongoing projects
      ~July: Review and new proposals*
Notes: You should state that the program is currently funded out of RHIC Operations funds and not additional funds that come to BNL.

## Slide 5: EIC Detector R&D Program in Numbers
  FY18: Record participation this time (expected)
    9 new proposals
    9 existing projects requesting continuation
  FY16-now: flat funding
  FY17, FY18:
    Total requested: ~$2.4M
LRP
Investment in program
so far ~$8M

## Slide 6: Detector Choices
General Purpose Detector
  While relatively well studied, requirements spread over various documents and not always up-to-date. Focus of R&D efforts.
  Design/Study efforts dominantly centered at JLAB and BNL
  Many open question
    1 or 2 detectors; if 2, different emphasis
    To fit into funding profile 2nd later?
Specialized Detectors
  Discussion has just started
arXiv:1212.1701
arXiv:1209.0757
arXiv:1409.1633
EIC User Group needs to get involved.
Whatever choice, it has impact on the machine design as well. May be a workshop later this year?

## Slide 7: Project: EIC Detector Handbook
“Living” document on requirements, R&D needs, available technologies, EIC kinematics and more
We started with a compilation of information that is available
Update as things become more refined
Right now: not even a draft
Current manpower: TU & A. Kiselev
Volunteers are more than welcome

## Slide 8: EIC Detector Requirements
Requirement are mostly site-independent with some slight differences in the forward region (IR integration)
In Short:
  Hermetic detector, low mass inner tracking, good PID (e and p/K/p) in wide range, calorimetry, forward & backwards tracking
  Moderate radiation hardness requirements, low pile-up, low multiplicity
p (GeV/c)
From R&D Handbook

## Slide 9: Electron Kinematics
e+p: 10 on 100 GeV
From R&D Handbook

## Slide 10: Hadron Kinematics
Here: e+p 15 on 250 GeV
From R&D Handbook
PID is one of the challenges for an EIC detector Þ R&D

## Slide 11: Compilation of EIC Detector Requirements
From R&D Handbook. Requirements as detailed in various documents (EIC WP, eRHIC and JEIC Design Reports).

## Slide 12: Detector Concepts
Concept Detectors
  Important as test bed for detector R&D
  Each attempt to match requirements
  Nothing is cast in stone
  Will evolve as new concepts are developed

## Slide 13: eRD1: Calorimetry
Goal: Develop cost effective, flexible techniques to build compact sampling calorimeters that meet the EIC physics requirements.
Efforts:
  Tungsten-scintillating fiber EM calorimeter (SPACAL)
    Compact calorimeter, developed at UCLA
    Investigating high resolution version for e-going endcap
  Crystal EMCal
    Option for high resolution e-going endcap calorimeter
  Shashlik EMCal
    Option for h-going endcap calorimeter
  HCal
    Prototype development in collaboration with STAR forward upgrade and sPHENIX
  Readout
    SiPM and APDs, radiation studies and support electronics
Participating institutions: BNL, Caltech, CUA, JLAB, IUCF, NPN Orsay, PSU, TAMU, UCLA, USTC, YPI

## Slide 14: W-SciFi Calorimetry
Scintillating fibers embedded in composite absorber
Round and square fibers tested
Test beam campaigns in 2015 and 2016
Square Fiber version achieves target of 7%/√E, with 1% constant term at 10o, 2.9% at 4o
2017: Optimizing light collection
In RHIC beam in 2017, h=3.75, ~1011 n/cm2)
Issue: SiPM show non-homogeneous degradations, PM by PM. APD?

## Slide 15: Crystal Calorimetry
e-going direction needs high precision calorimetry (~2%/√E)
PbWO calorimeter option for this role, extensively used for high precision calorimetry (CMS, JLab, PANDA…) because of its excellent energy and time resolutions and its radiation hardness
BTCP (Russia) produced high quality crystals in the past but out of business
SICCAS (China) has difficulties maintaining good crystal quality
Collaborative effort with PANDA to qualify CRYTUR (Czech Republic)
Full size (2x2x20 cm3) CRYTUR crystal
Participating institutions: YPI, CUA, IPN-Orsay, JLAB, BNL, Caltech
2017: chemical analysis ongoing
CUA: growing crystals for faster turnaround time?
See C. Munoz-Camacho , Parallel 1

## Slide 16: eRD2: A Magnetic Field Cloaking Device
To retain good momentum resolution in the forward region, need dipole field
Dipole fields affect beam optics
Develop magnetic cloak
Method: Wrapping layers of AMSC high-temperature superconductor around beam pipe
BNL van de Graaff
External dipole
field 30 mT
Beam shielding tests with the BNL Van de Graaff accelerator
Institutions: Stony Brook, BNL, RIKEN
See talk by Nils Feege, Parallel 1

## Slide 17: Magnetic Field Cloaking Device
High-field shielding and cloaking tests with MRI magnet at ANL
Shield a 0.5 T field with a 10 cm SC cylinder at liquid nitrogen temperature.
Multi-layer shield
Project has demonstrated magnetic field cloaking with 99% field shielding and 90% reduced field distortions next to the shield at 0.45 T
Magnetic field cloak seems to be a viable option for EIC. Design parameters, fabrication, and limitations understood
Project concluded: arXiv:1707.02361, submitted to NIM

## Slide 18: eRD3: MPGD Based Tracking
Development of intermediate tracking system
  Barrel tracking system based on Micromegas; curved MM R&D program in close collaboration with Saclay
  Forward/Backward tracking system based on triple-GEM
Design and assembly of large cylindrical MM detector elements to demonstrate scaling of technology
Test and characterization of MM chambers with full readout chain based on DREAM chip
Participating Institutions:
Temple Univ., Saclay
MicroMegas (MM):

## Slide 19: MPGD Based Tracking
Triple-GEM detector assembly 40x40cm designed
GEM foils from TechEtch and CERN
Close collaboration with industry (TechEtch)
Quality assurance of GEM foils developed based on automatic CCD scanning system
Assembly of triple-GEM chamber with full stacking and cosmic ray test with full readout chain

## Slide 20: eRD16 & eRD18: Silicon Tracking
Silicon Detector Layout Investigations
  Performance requirements: numbers of layers, layout and spatial resolution of the pixel hits
Institutions: eRD16: LBL, eRD18: Birmingham
Studies
  Using toolset originally developed for ILC: Helix track model, multiple scattering, full track reconstruction from digitized hits using a Kalman filter.
  Currently assuming ALPIDE chip
  Study includes pileup (integration time)

## Slide 21: eRD16 & eRD18: Silicon Tracking
Sensor Development
  Aim: to demonstrate high spatial resolution in a fully depleted sensor
  Advantage of depletion = charge collection by drift Þ larger Q, fast collection, small cluster multiplicity
  Starting point: ALPIDE sensor (ALICE ITS)
  TowerJazz modified process: First results indicate full depletion
  Technology strong contender for dedicated EIC MAPS prototype
  Exploit on-going ATLAS R&D in Birmingham
Alpide:

## Slide 22: eRD6: ZigZag Strip Readouts
Improve on the position resolution of GEM readout boards with novel design
  Implement zig-zag readout; test with 3-GEM readout and X-ray source
  Optimization of the zigzag pad readout pattern parameters, fabrication of PCB with this readout pattern and measurement of the relative position resolution in the lab
  Recent: Scans of PCBs with improved zigzag strip design achieve < 70 μm spatial resolution
  Still suffer from single pad hits in regions near center of pad (due to low gain, non-optimal interleaving, small transverse diffusion, etc)
eRD6: BNL, FIT, INFN Trieste, SBU, UVa, Yale

## Slide 23: eRD6: Cherenkov TPC
Combines the functions of a TPC for charged particle tracking and a Cherenkov detector for particle identification in same volume
Prototype:
  TPC: 10cm drift + 10x10 cm2 4 layer GEM
  Cherenkov: 3.3 x 3.3 cm2 pad array + 10 x 10 cm2 4 layer GEM
  Common Gas: CF4 (vdrift = 7.5 cm/μs & large N0)
Successful demonstration of proof of principle - TPCC works!
Finalizing performance specs on track resolution and Cherenkov light yield, paper in progress

## Slide 24: eRD6: Mini-Drift GEM Tracking Detector
  Triple GEM stack with a small drift region (mini TPC type configuration)
  Position and arrival time of the charge deposited in the drift region were measured on the readout plane allowing reconstruction of track traversing the chamber.
  Minidrift overcomes resolution degradation with incident angle for conventional GEM tracking detectors using only charge centroid information.
  Compatible with all forms of planar GEM tracker.
Normal Chamber
MiniDrift

## Slide 25: eRD6: MPGD-Based Photon Detector for RICHs
Motivation
  h-PID in the range 6 < p < 60 GeV/c, a must for EIC
  At high momenta: gas radiator is mandatory
  Collider detector: short (~ 1 m) radiator length
R&D program
  Development of MPGD-based Photon Detectors
    Miniaturized pads
    Operation in C-F gases
    THGEM vs GEM for optimal photoelectron collection
    Ion BackFlow (IBF) control
    Photocathodes: alternatives to CsI?
      CsI: aging, doesn’t tolerate water vapor, O2

## Slide 26: eRD6: MPGD-Based Photon Detector for RICHs
New activity at INFN Trieste
  Design of prototype of MM with resistive layer and miniaturized pad-size well advanced
New photocathode
  Hydrogenated diamond film: Spray technique making use of NanoCrystals powder at T ~ 120° (instead of std >800° )
  Next steps: Coupling of photo converter and MPGDs
47%
see Stefano Levorato , Parallel 1

## Slide 27: eRD14: PID Consortium
  Particle ID is essential for EIC
Developing a suite systems covering the full angular- and momentum range required Imaging Cherenkov detectors are the primary technology
Current Projects
  h-side: RICH with two radiators (gas + aerogel) are needed to cover the full momentum range: more than 3 s.d. separation for π/K/p over 3-50 GeV/c
  e-side: Compact aerogel RICH covering up to 10 GeV/c (π/K/p) can provide the required PID optimized for EIC physics requirements
  Barrel:
    DIRC is compact and can cover momenta up to 6-7 GeV/c
    ToF issue with determining T0
Institutes: ACU, ANL, BNL, CUA, William & Mary, Duke, GSU, GSI, Howard, INFN Ferrara, INFN Roma, ISS Rome, JLAB, LANL, ODU, USM, UIC, UNM, SC, Yale
e-endcap
h-endcap
barrel
10x100 GeV
Q2 > 1 GeV2
DIRC
Aerogel RICH
Dual-radiator RICH
p/A
e
GeV
rapidity

## Slide 28: eRD14: dRICH
First dual-radiator RICH developed for use with solenoidal detector
Combination of C2F6 gas and n=1.02 aerogel leaves no gaps in coverage
Outward-reflecting mirrors reduce backgrounds and (UV) scattering in aerogel
3D focusing reduces photosensor area
Geant4 sims show excellent performance for hadron and lepton ID
G4 sims include B field
See Alessio Del Dotto, Parallel 1

## Slide 29: … and many more
eRD6: Large forward GEM tracker prototype
eRD6: Development of large cylindrical μ-RWELL
eRD6: Chromium GEM foils
eRD12: Electron polarimeter, luminosity monitor and a low Q2-tagger (concluded)
eRD14: Modular aerogel RICH (mRICH) - see Cheuk-Ping Wong, Parallel 1
eRD15: Compton electron detector for polarimetry - see Nicola Minafra, Parallel 1
eRD17: BeAGLE, Tool to refine detector requirements for eA in the saturation regime
eRD19 & New Proposal: Machine background studies
eRD20 - Developing simulation and analysis tools - see Markus Diefenthaler, Parallel 1
and then some …

## Slide 30: Take Away Message
The Good
The EIC physics has many characteristics that are unique to the environment and need dedicated R&D.
High quality and highly relevant R&D being carried out within the EIC R&D program.
Good involvement of universities and national laboratories; excellent student involvement, good publication record.
The Bad
The program is at the tipping point. The number of proposals increases steadily while the funding stays flat. We either spread the funding thin (ineffective), or we fund fewer (discourages many, exclude groups we want on board). Neither option is good for the EIC.

## Slide 31: Afterthoughts
With the publication of the LRP came a significant increase in international and national participation.
With a (hopefully) positive outcome of the NAS review the number of proposals and groups will certainly go up further.
Many of the participating groups will be an important part in the formation of EIC collaborations and will likely be those that form detector groups.
We suggested to DOE an increase towards a $3-4M/year level within 3-4 years if possible. International support will help, but the US has to take the lead (increased R&D funding was recommendation in LRP ’15)
Strengthening the R&D program would ensure that the technologies exists and are mature enough to carry out the EIC physics program.